LM-86

Professional Microphone Instruction Manual with Prelude Light Ring Indicating Conference

This product is designed and manufactured for meeting, speech, broadcast, recording and other occasions. Its unique prelude sound prompt function and light ring indication, coupled with high-fidelity circuit and imported electret capsule, fully realize its multi-functional, novel appearance and high quality characteristics.

The main parameters:

Energy conversion method: electret

Directivity: heart-shaped pointing

Frequency response: 40~16000Hz

MIC sensitivity: -43dB±2dB

Prelude sensitivity: -50dB±2dB

Power supply voltage: DC9V/AC220V

Audio cable length: 10m

Instructions:

1. Connect the audio signal cable and connect it with the MIC jack in the audio equipment.

2. First put the MIC volume knob of the power amplifier to the "0" position, and then plug in the external power supply.

3. Press the microphone switch, the light ring is on, and the microphone can send calls at this time, adjust the volume of the audio equipment while shouting into the microphone, until the best effect is achieved. There is a prelude switch on the base of this product, and a MIC adjustment potentiometer, which can be adjusted to an appropriate volume.